## Slide 1
Industrial PC
Advantech UNO-1372G-J
Celerron J1900 2.0Ghz
8GB DDR3L Memory
2 Gb Ethernet
4 RS232/422/485 (isolated)
CAN Card
Advantech PCM-26D2CA-AE
2 Port Isolated CANBus
miniPCIe
DSub9 2EA
Motor Driver
DIS-2 48/10 FB (Metronix, 독일)
20-60 VDC
Rated 15 Arms/Peak 40 Arms
CE certificate
Motor Driver
DIS-2 48/10 FB (Metronix, 독일)
20-60 VDC
Rated 15 Arms/Peak 40 Arms
CE certificate
Motor
Motor

## Slide 2
Connector | 용도
X1 | Main Power, Logic Power, Digital In/Out
X2 | Encoder, Hall Sensor
X3 | Brake
X301~X302 | Motor U/V/W
X304 ~ X305 | Brake Registor
X401 | CAN in
X402 | CAN out
Housing | Frame Ground
X5 | RS-232, 설정용
회생저항
푸름
MCRA-100-N5ΩF-300
5Ω 100W
종단저항
삼원액트
M12C-MDN-TR
M12, A-code, 5 pin, 120 Ω
M12 케이블
삼원액트
M12C-ADN-V010
M12, A-code, 5 pin, Male-Female, 1 meter
M12 케이블
삼원액트
M12C-GDN-V010
M12, A-code, 5 pin, Male-Free end, 1 meter
끝단에 DSub9 단자 연결
X1 커넥터
Pheonix Contact
1855102 1EA, Housing
1852820 2EA, 8pin
1852846 1EA, 2pin
1852901 1EA, frame
1853926 1EA, PG21 Clamp

## Slide 3
통신부
RS-485
RS-232
CAN
RS-232
Ethernet
주행모터 제어기
바코드
카메라
배터리
장애물감지 스캐너
조향모터 제어, IO, 이적재부 등
전후륜 동기제어부
경로지도 파일
경로 탐색부
속도궤적 생성부
(가감속/장애물 감지)
로그/파라미터
파일
1번 위치로 가라
장애물로 인해 감속해라
장애물로 인해 멈춰라
잠시 멈취라
자동/수동 모드
수동 조작
IPC (Windows 10 IoT)
경로지도 예시
조향모터 돌려라
현재 위치
현재 속도
OCS 통신
이적재부 동작
Safety
장애물 감지
표시등, 부저
배터리 상태
충전 조작
수동조작 UI
IO 통신
<선행기술팀>
C++/DLL(?)
<소프트웨어 개발팀>
C#
파라미터 설정(통신)

## Slide 4
Safety 회로 (참고)