## Slide 1: OHV (Over Head Vehicle) SYSTEM PROPOSAL
Oct 14 , 2019
GSI Co., Ltd.
GSI ‘19年

## Slide 2
CONTENTS
Revision Sheet
General Description
1. System Overview
1-1. System Overview
1-2. Vehicle Route & Cycle Time
2. System Configuration
2-1. OHV System Configuration
2-2. Maintenance Lifter
2-3. Work Lifter & Work Shuttle
2-4. Data Matrix Positioning System
2-5. Charging Station & Collector
2-6. Power Supply Unit (Battery)
2-7. On-Line System
3. Utility Specification

## Slide 3
REVISION SHEET
■ Equipment Name : OHV SYSTEM
■ Customer’s Reference No. :
■ Manufacturing No. :
■ Rev. No. : REV. 2
■ Issued No. : 190917
■ Customer (Approval)
Received by : Date : / / .
Authorized by : Date : / / .
REV. No. | 주요 변경 내역 | DATE
0 | ▶ 초안작성 | 2019. 09. 17
1 | ▶ Lay Out 변경 | 2019. 10. 07
2 | ▶ Lay Out 변경 | 2019. 10. 14

## Slide 4
GENERAL DESCRIPTION
1-1. SYSTEM OVERVIEW
No | DESCRIPTION | SPECIFICATION | REMARK
1 | Application Process | OHV (Overhead Vehicle) System | 
2 | Work Spec. | 자재 Box ( 850(L) x 650(W) x 500(H) ) | 
3 | Pass Line | Pass Line : 2134.5mm (천정으로부터 1,000mm 내 구성) | 천정고 : 3M
4 | Configuration | 1) Rail : Closed Loop R_190m / L_210m (Straight, Curve, Branch & Safety Fence) | 
 |  | 2) Vehicle Quantity : Total 8 Set -. Right Rail : 4 Set (Operation 3 Set / Charging 1 Set) -. Left Rail : 3 Set (Operation 2 Set / Charging 1 Set) -. Spare : 1 Set | 
 |  | 3) Ports ( Work Lifter ) : Total 14 Set -. Right Rail : 8 Set -. Left Rail : 6 Set | 
 |  | 4) Vehicle Maintenance Lifter ( MTL ) : Right 1 Set, Left 1 Set | 
 |  | 5) Maintenance Branch : Right 2 Set, Left 2 Set | 
 |  | 6) Charging Station : Right 1 Set, Left 1 Set - Battery Power Supply Only ※ 지정된 충전위치 외에 Vehicle 대기 위치 상에서 수시 충전 | 
5 | Vehicle Power Supply | Battery Power Supply Type – 별도의 Charging Station 및 충전 대기 Vehicle 필요 | 
6 | Shuttle (Vehicle) Driving Speed | Straight : Max. 180m/min (3,000mm/sec) | 
 |  | Curve : Max 35m/min (583mm/sec) | 
 |  | Acceleration (Deceleration) : 1m/sec2 (0.1G) | 
7 | Control | MTL, Vehicle & Work Lifter : PLC Sequence Control | 
 |  | OCS, CIM : PC Control | 
 |  | Vehicle to Main Controller (PLC) Communication : Wireless Wifi | 
 |  | OCS to Main Controller (PLC) Communication : CC Link IE | 

## Slide 5
1-2. VEHICLE ROUTE & CYCLE TIME
VEHICLE DRIVING SPEED
-. Straight Driving Speed :
Max 180m/min (3000mm/sec)
-. Curve Driving Speed :
Max 35m/min (580mm/sec)
-. Acceleration (Deceleration) Speed : 1m/sec²
GENERAL DESCRIPTION
■ VEHICLE ROUTE

## Slide 6
1-2. VEHICLE ROUTE & CYCLE TIME
GENERAL DESCRIPTION
■ VEHICLE CYCLE TIME & VEHICLE 필요수량
항목 |  |  |  |  | 자재교체주기 (Hr) | 자재필요 (Min) | 자재필요횟수 (1Day) | OHV 수량 -. 1Loop이송=4Min기준(Hr가능=15회) -. 1Day=360회 (가동 율 100%) -. 1Day=241.2회 (가동 율 67%) | 비고
Right 권취 + CAN | 권취 (1) | 1 | TAB(4) | 1 | 6.9 | 414 | 3.5 |  | 241.2
 |  |  |  | 2 | 6.1 | 366 | 3.9 |  | 
 |  |  |  | 3 | 7.8 | 468 | 3.1 |  | 
 |  |  |  | 4 | 11.4 | 684 | 2.1 |  | 
 |  | 2 | TAB(6) | 1 | 6.9 | 414 | 3.5 |  | 
 |  |  |  | 2 | 9.9 | 594 | 2.4 |  | 
 |  |  |  | 3 | 7.7 | 462 | 3.1 |  | 
 |  |  |  | 4 | 12.6 | 756 | 1.9 |  | 
 |  |  |  | 5 | 34.1 | 2046 | 0.7 |  | 
 |  |  |  | 6 | 11.4 | 684 | 2.1 |  | 
 |  | 3 | SEPARATOR |  | 1.1 | 66 | 21.8 |  | 
 | 조립 | 4 | CAN |  | 0.2 | 12 | 120.0 |  | CAN
 | 권취 합계(4대기준) |  |  |  |  |  | 672.6 | 2.8 | OHV수량=3대
Left 권취 + 조립 | 권취 (1) | 1 | TAB(4) | 1 | 6.9 | 414 | 3.5 |  | 
 |  |  |  | 2 | 6.1 | 366 | 3.9 |  | 
 |  |  |  | 3 | 7.8 | 468 | 3.1 |  | 
 |  |  |  | 4 | 11.4 | 684 | 2.1 |  | 
 |  | 2 | TAB(6) | 1 | 6.9 | 414 | 3.5 |  | 
 |  |  |  | 2 | 9.9 | 594 | 2.4 |  | 
 |  |  |  | 3 | 7.7 | 462 | 3.1 |  | 
 |  |  |  | 4 | 12.6 | 756 | 1.9 |  | 
 |  |  |  | 5 | 34.1 | 2046 | 0.7 |  | 
 |  |  |  | 6 | 11.4 | 684 | 2.1 |  | 
 |  | 3 | SEPARATOR |  | 1.1 | 66 | 21.8 |  | 
 | 조립 | 1 | CID |  | 0.7 | 42 | 34.3 |  | 
 |  | 2 | GACKET |  | 0.8 | 48 | 30.0 |  | 
 |  | 3 | 절연판 | 하절연판 | 24 | 1440 | 1.0 |  | 
 |  |  |  | 상절연판 | 8 | 480 | 3.0 |  | 
 |  | 4 | TUBING |  | 12 | 720 | 2.0 |  | 
 |  | 5 | WASHER |  | 12 | 720 | 2.0 |  | 
 |  | 6 | 부직포 |  | 8 | 480 | 3.0 |  | 
 | 조립 합계(4대기준) |  |  |  |  |  | 493.7 | 2.0 | OHV수량=2대

## Slide 7
1-2. VEHICLE ROUTE & CYCLE TIME
GENERAL DESCRIPTION
Work Lifter ( 8 Ports )
Work 회수 Line
MTL
Work 공급 Line
자재 STK (1Port)
VEHICLE 운영 (권취 + 조립)
-. Operation 2 Set / Charging 1 Set
Maintenance Branch ( 2 Port )
Charging Branch ( 1 Port )
회귀 구간
■ LEFT RAIL CONFIGURATION

## Slide 8
Work 공급 Line
1-2. VEHICLE ROUTE & CYCLE TIME
GENERAL DESCRIPTION
Work Lifter ( 4 Ports )
Work 회수 Line
MTL
자재 STK ( 1Ports )
Work Lifter Can 전용 ( 2 Ports )
Charging Branch ( 1 Port )
회귀 구간
Maintenance Branch ( 2 Ports )
VEHICLE 운영 (권취 + CAN)
-. Operation 3 Set / Charging 1 Set
■ RIGHT RAIL CONFIGURATION

## Slide 9
1-2. VEHICLE ROUTE & CYCLE TIME
GENERAL DESCRIPTION
Tray 공급
Tray 회수
Work Lifter
OHV RAIL CONCEPT & VEHICLE 상공위치
-. VEHICLE PASS LINE : 2,135mm
■ RAIL CONCEPT & VEHICLE POSITION

## Slide 10
2-1. OHV SYSTEM CONFIGURATION
■ Layout & Unit Configuration
SAFETY FENCE
VEHICLE RAIL
VEHICLE
YOKE
CEILING SUPPORT
SYSTEM CONFIGURATION

## Slide 11
※ Straight Rail Level (Flatness) : ± 0.2mm
Safty Fence SUS PIPE
OHT Rail(압출 Profile)
Safty Mesh망
Parallel Rail 고정 Support
Ceiling Support
DESCRIPTION | SPECIFICATION | REMARK
RAIL & SAFTY FENCE | Driving Rail : AL6061 압출 Profile | 
 | Parallel Rail 고정 Support : Standard Yoke | 
 | Ceiling Support : AL6061 사출품 | 
 | Safty Fence : SUS Pipe & Mesh 망 | 
2-1. OHV SYSTEM CONFIGURATION
■ Rail & Safety Fence Unit (Concept)
SYSTEM CONFIGURATION

## Slide 12
Tray 투입 & 배출
※ Drive Wheel 교체주기 : 6개월 내 (PM 주기)
DESCRIPTION | SPECIFICATION | REMARK
VEHICLE | Driving Method : Servo Motor & Wheel | 
 | Driving Speed : Straight, Max. 3,000 mm/sec | User Spec.
 | Driving Speed : Curve, Max. 580 mm/sec | 
 | Acceleration (Deceleration) Speed : 1m/sec² | 
 | Vehicle Guide Roller : Urethane | 
 | Wheel Steering Unit : Installed | 
 | Corner Driving Differential : Wheel 개별 구동 | 
DIRECTION
Tray 이송 Conveyor
Servo Motor
(2개소)
Driving Wheel
Rail Guide Roller
2-1. OHV SYSTEM CONFIGURATION
■ OHV Vehicle Unit (Concept)
SYSTEM CONFIGURATION

## Slide 13
VEHICLE 투입 & 배출
2-2. MAINTENANCE VEHICLE LIFTER (CONCEPT)
SYSTEM CONFIGURATION
VEHICLE 투입 & 배출

## Slide 14
2-3. WORK LIFTER & WORK SHUTTLE (CONCEPT)
SYSTEM CONFIGURATION
Tray 공급
Tray 회수
Work Shuttle
Work Lifter

## Slide 15
2-3. WORK LIFTER & WORK SHUTTLE (CONCEPT)
SYSTEM CONFIGURATION
Work Rack
회수 Work 물류
공급 Work 물류
DESCRIPTION | SPECIFICATION | REMARK
Work Shuttle | Driving Method : Y Axis Servo Motor | 
 | 투/배출 Conveyor : Induction Motor | 2 Set
Work Lifter | Driving Method : Z Axis Servo Motor | 
 | 투/배출 Conveyor : Induction Motor | 1 Set
Work Lifter <->Vehicle 투/배출
( Work 공급 및 회수)
Work Lifter ->Work Shuttle 배출
( Work 공급)
Work Lifter <- Work Shuttle 투입
( Work 회수)

## Slide 16
DESCRIPTION | SPECIFICATION | REMARK
OPTICAL READING HEAD | Passage Speed : v ≤ 8m/s | 
 | Measuring Range : Max 10000m | 
 | Light Type : Integrated LED Lightning (red) | 
 | Scan rate : 40 s-1 | 
 | Read distance : 100 mm | 
 | Depth of focus : ± 50 mm | 
 | Reading field : 115 mm x 73 mm | 
 | Ambient light limit : 100000 Lux | 
 | Accuracy : ± 0.2 mm | 
2-4. DATA MATRIX POSITIONING SYSTEM
SYSTEM CONFIGURATION
■ QR BAR CODE READER

## Slide 17
2-5. CHARGING STATION & COLLECTOR
SYSTEM CONFIGURATION
CHARGING STATION
■ CHARGING STATION
■ CHARGING BASE & COLLECTOR (MAKER : ROBOTEQ)
COLLECTOR
CHARGING BASE
CHARGING BASE
COLLECTOR
N S N
N S N
N
N
RAIL
▶ VEHICLE 진입 시
▶ VEHICLE 정위치 시
CHARGING BASE & COLLECTOR
CHARGING BRANCH
※ MAGNET을 이용하여,
VEHICLE 정 위치 시
COLLECTOR CONTACT

## Slide 18
2-6. POWER SUPPLY UNIT
SYSTEM CONFIGURATION
■ VEHICLE BATTERY
BATTERY 선정조건 1) VEHICLE MOVING SPEED -. Straight Moving Speed : Max. 180m/min (3,000mm/sec) -. Curve Moving Speed : Max. 35m/min (583mm/sec) -. Acceleration (Deceleration) Speed : 1m/sec2 (0.1G) 2) VEHICLE 가동률 -. 가동시간 : 4Hr (완충 후 운영 가능 시간) -. 충전시간 : 2Hr (완충 소요 시간) -. 가동률 : 4/(4+2)*100 = 67% ( 수시충전 포함 )
선정 BATTERY & CHARGER 1) BATTERY : 25V, 1320Wh 2) CHARGING UNIT : 700W-25V25A

## Slide 19
2-6. POWER SUPPLY UNIT
SYSTEM CONFIGURATION
■ BATTERY 기본 운영
MAIN BATTERY
BACKUP BATTERY
POWER
BATTERY 충전시
MAIN BATTERY
AGV 구동 회로
평상시
AGV 구동 회로
MAIN BATTERY
BACKUP BATTERY
정상 운영시
MAIN BATTERY
AGV 구동 회로
평상시
AGV 구동 회로
POWER
MAIN BATTERY
BACKUP BATTERY
MAIN BATTERY 방전시
MAIN BATTERY
AGV 구동 회로
평상시
AGV 구동 회로
POWER
POWER
-. RS-232/485 통신 기능 내장 형 BATTERY 사용  BATTERY 상태 MONITORING 가능.
-. BATTERY 잔량이 일정 수준 이하인 경우, 운행을 중지하고 자동으로 충전 시작 (충전 위치로 이동)
※ BATTERY 운영시간을 연장을 위해서, 충전 위치 외에, 대기위치상에서도 수시충전
■ BATTERY 방전 시 대책
-. AGV 내부 BACK-UP BATTERY 를 별도 설치하여, MAIN BATTERY 방전 시 단 시간 동안 BACK-UP BATTERY로
AGV 운영 (충전 STATION 으로 이동)
-. PORTABLE 보조 BATTERY 를 이용한 전원공급
※ 보조 BATTERY 이용한 VEHICLE 이동 시 편의성을 위한 MCU 기본 제공

## Slide 20
ADS (TC)
OCS &
MONITORING SYS.
MAIN PLC
AP
HUB
MAIN CONTROLLR
MTL(LIFTER)
※ OCS (OHV Control System) : OHV System을 운영하기 위한 물류제어 Software.
※ HUB : Network를 구성하기 위해 OCS운영 PC와 OHV System 장치들을 LAN에 접속시키는 공유장치.
※ AP (Access Point) : OCS운영PC와 OHV간의 통신을 위한 무선 LAN 안테나.
SYSTEM CONFIGURATION
2-7. ON-LINE SYSTEM CONFIGURATION
VEHICLE
WORK LIFTER (PORTS)
OHV SYSTEM
CC LINK IE
ETHERNET
ETHERNET
WIRELESS
ETHERNET

## Slide 21
Utility | Usage | Size | Q’ty | Specification | Max. Volume | Material | Connection
Air | Operation | ½” | 1 | 0.55 ~ 0.6 Mpa | 250 NLPM | SUS Tube | ½” LOK Fitting
Power (GPS) | 3PH 220VAC, 50/60Hz, 8.6 KVA (23A) |  |  |  |  |  | Terminal Block
Power (UPS) | 1PH 220VAC, 50/60Hz, 1.1 KVA (5A) |  |  |  |  |  | 
UTILITY SPECIFICATION
3. UTILITY SPECIFICATION
■ VEHICLE POWER SUPPLY (BATTERY)

## Slide 22
감사합니다